## Slide 1: Precision Agriculture Solutions- ESNav5.0
EFIX AG TEAM

## Slide 2
CONTENTS
MAIN INTERFACE
QUICK GUIDE
NEW FEATURES

## Slide 3
1.MAIN INTERFACE

## Slide 4
MAIN INTERFACE
SOFTWARE BROWSING
1
Implement settings
2
New guideline
3
Field management
4
Parameter settings
5
UI settings
6
Settings center
7
About
8
Guidelines switch
9
Painting
10
Line offset/RZ
11
Advanced U-Turn
12
Painting Color
13
Markers
14
Trajectory Recording

## Slide 5
MAIN INTERFACE
SOFTWARE BROWSING
19
Worked Area
15
GNSS status
16
Lateral deviation
18
Real-time speed
17
Guideline number
20
Compass
22
Vehicle locking
21
Demo speed slider
23
Zoom in/out
24
Auto/manual button

## Slide 6
2. QUICK GUIDE

## Slide 7
QUICK GUIDE
GNSS MODE
GNSS MODE

## Slide 8
QUICK GUIDE
GNSS MODE
Go to [Agriculture management]---[GNSS]
1. Multiple constellations with GPS/GLONSS/BDS/GALILEO/QZSS enable/disable;
2. Clear ephemeris to reset the GNSS board;
3. Mulitple work modes with SPP, DGPS, RTK, EPPP, HPPP and DRSMOOTH.

## Slide 9
QUICK GUIDE
GNSS MODE
Go to [Agriculture management]---[GNSS]
1. Multiple constellations with GPS/GLONSS/BDS/GALILEO/QZSS enable/disable;
2. Clear ephemeris to reset the GNSS board;
3. Mulitple work modes with SPP, DGPS, RTK, EPPP, HPPP and DRSMOOTH.

## Slide 10
QUICK GUIDE
VEHICLE
VEHICLE

## Slide 11
QUICK GUIDE
VEHICLE
Go to [Vehicle]---[New] to create a new vehicle
1. Select one vehicle type with Front Steer, Rear Steer, Tracked, Aticulated, Transplanter;
2. Set vehicle brand, model and name;
3. Ultra-low speed mode with supporting minimum 0.1KM/H speed.
VEHICLE SELECTION

## Slide 12
QUICK GUIDE
VEHICLE
VEHICLE CONTROL
1. Select the steering control method:
Motor/Hydraulic(PWM)/CANBUS;
2. Select the wheel angle sensor mode:
Potentiometer/GASensor/Without WAS.

## Slide 13
QUICK GUIDE
VEHICLE
VEHICLE PARAMETERS
A: Distance between front and rear axle.
B: Distance from rear axle to mount point.
G: The distance between the front wheels center lines.
Maximum WAS: The maximum angle vehicle can turn.
Locking line reference point: Vehicle rear or head

## Slide 14
QUICK GUIDE
VEHICLE
VEHICLE STEERING CALIBRATION
1. The calibration requires an open, flat and hard ground about 10*30 meters.
2. Keep the tractor run at 2km/h and click [Start]. During the process, the steering wheel will turn automatically.
3. When the screen shows “Waiting for calibrating…”, around 2 minutes later, the calibration will be successful.

## Slide 15
QUICK GUIDE
VEHICLE
VEHICLE INSTALLATION CALIBRATION
1. The calibration requires an open, flat and hard ground about 10*30 meters.
2. Click [Start] and it will set a guideline automatically. The vehicle will get into the auto mode.
3. When the distance from start is over 30m, stop the vehicle, click [Next]. Then it will record the END point and switch to manually mode.

## Slide 16
QUICK GUIDE
VEHICLE
VEHICLE INSTALLATION CALIBRATION
4.Turn around and back to the same guideline. After enter the line, click [Next] and the it will switch to Auto mode.
5.Then drive forward automatically and keep the speed between 2-3km/h.
6.Stop the vehicle when the distance from start point is below 1m. Click [End], the system will complete automatically.

## Slide 17
QUICK GUIDE
IMPLEMENTS
IMPLEMENTS

## Slide 18
QUICK GUIDE
IMPLEMENTS
Go to [Implement]---[New] to create a new implement
Info:
a. Manage/new implements or view implements details on this interface.
b. Supports to export implements information.
IMPLEMENTS

## Slide 19
QUICK GUIDE
IMPLEMENTS
IMPLEMENT SELECTION
Job type:
Spraying/Ridge building/Planting/Spreading Harvest/Scatter sowing/Water and fertilizer/Tilling
Mounting method: Rear/Front/Single point mounted

## Slide 20
QUICK GUIDE
IMPLEMENTS
IMPLEMENT PARAMETERS
A: Implement width
B: Row spacing (The distance between two passes)
C: Hitch point (The distance from hitch point to implement, just keep the default value 0 )
D: Implement center offset

## Slide 21
QUICK GUIDE
IMPLEMENTS
IMPLEMENT ROW SPACING AUTO ADJUSTMENT
Auto calculation
If there is the row spacing issue with skip or overlap, it is necessary to click [Calculate] to make offset calculation.
There are two methods to choose, then follow the instruction.

## Slide 22
QUICK GUIDE
FIELDS
Info:
a. Manage/new fields or view fields details on this interface.
b. Supports to export fields
Go to [Field]---[New] to create a new field

## Slide 23
QUICK GUIDE
GUIDELINES
Go to [Field]---[New] to create a new field

## Slide 24
3. NEW FEATURES

## Slide 25
NEW FEATURES
CLOUD SERVICES
CLOUD SERVICES

## Slide 26
NEW FEATURES
CLOUD SERVICES
Register & Login in ESNAV5.0
1. Login in PC webpage
2. Check the real-time tractor lcoation
3. Create a new field
4. Send it to the terminal

## Slide 27
NEW FEATURES
CLOUD SERVICES
Register & Login in ESNAV5.0
1. Login in PC webpage
2. Check the real-time tractor lcoation
3. Create a new field
4. Send it to the terminal

## Slide 28
NEW FEATURES
DATA TRANSFER
DATA TRANSFER

## Slide 29
NEW FEATURES
DATA TRANSFER
Import file data
Import by share code
Export file data Export by share code

## Slide 30
NEW FEATURES
DATA TRANSFER
When import/export file, currently SHP and ISOXML file are supported.

## Slide 31
NEW FEATURES
AUTO U-TURN
AUTO U-TURN

## Slide 32
NEW FEATURES
AUTO U-TURN
Automatic U-turn switch: The option to enable/disable Auto U-turn
U-Turn type:
AB line U-turn
A+ line U-turn
Boundary U-turn
Headline U-turn

## Slide 33
NEW FEATURES
AUTO U-TURN
1. U-shaped mode
2. Alternate mode
3. One-way mode
AB U-TURN

## Slide 34
NEW FEATURES
AUTO U-TURN
A+ U-TURN
1. U-shaped mode
2. Alternate mode
3. One-way mode
4. Able to set U-Turn direction and rows manually

## Slide 35
NEW FEATURES
AUTO U-TURN
BOUNDARY U-TURN
1. U-shaped mode
2. Alternate mode
3. One-way mode
4. Set the distance to the boundary

## Slide 36
NEW FEATURES
AUTO U-TURN
HEADLINE U-TURN
1. U-shaped mode
2. Alternate mode
3. One-way mode
4. Whether exceeds the boundary

## Slide 37
NEW FEATURES
SAFETY
SAFETY

## Slide 38
NEW FEATURES
SAFETY
Maximum speed allowed to enable Auto U-Turn
When the vehicle speed is more than the threshold, the Auto U-Turn will not be able to triggered.

## Slide 39
NEW FEATURES
BOUNDARY CREATION
BOUNDARY CREATION

## Slide 40
NEW FEATURES
BOUNDARY CREATION
Create a new boundary with different implement location

## Slide 41
NEW FEATURES
BOUNDARY CREATION
1. Able to plan straight line and curve line
2. Able to add mark point on the boundary

## Slide 42
NEW FEATURES
BOUNDARY CREATION
1. Set the headline with maximum 10
2. Snap points to create AB lines on the boundary

## Slide 43
NEW FEATURES
ACCESS PATHS
ACCESS PATHS

## Slide 44
NEW FEATURES
ACCESS PATHS
Drainage ditch scenarios each three rows

## Slide 45
NEW FEATURES
ACCESS PATHS
1. How many lines per access path
2. Access path width
3. Rows in the first group
4. Line place in first group

## Slide 46
NEW FEATURES
ACCESS PATHS
1. How many lines per access path
2. Access path width
3. Rows in the first group
4. Line place in first group

## Slide 47
NEW FEATURES
TRAMLINE
TRAMLINE

## Slide 48
NEW FEATURES
TRAMLINE
The principles of tramlines, they are placed in the field at seeding time. The width of the sprayboom has to be evenly divisible by the drill/air-seeder width, for example a 30' air-seeder and a 60'spray boom or a 40'air-seeder and a 120'spray boom.

## Slide 49
NEW FEATURES
TRAMLINE
1. Swath spacing
2. Offset
3. Initial swath

## Slide 50
NEW FEATURES
TRAMLINE
1. Set the original line in the main interface Line Offset Settings;
2.The Tramline will be highlighted.

## Slide 51
NEW FEATURES
ISOBUS UT & TC-SC
ISOBUS UT & TC-SC

## Slide 52
NEW FEATURES
ISOBUS UT & TC-SC
ISOBUS enable/disable

## Slide 53
NEW FEATURES
ISOBUS UT & TC-SC
Manual section control

## Slide 54
NEW FEATURES
ISOBUS UT & TC-SC
Auto section control

## Slide 55
NEW FEATURES
LANDMARK
LANDMARK

## Slide 56
NEW FEATURES
LANDMARK
1. Different markers can be configured in the Landmark Library;
2. Setting the marker reference in Recording Position.
View and manage landmark.

## Slide 57
NEW FEATURES
LANDMARK
It is avaliable to set markers in the mainterface by shortcut icon

## Slide 58
NEW FEATURES
TRAJECTORY RECORDING
TRAJECTORY RECORDING

## Slide 59
NEW FEATURES
TRAJECTORY RECORDING
Record real-time track 3D coordinates, which can be exported in txt and shp formats.
In Brazil, many customers want to record the real track when do auto steering because some ground may be not flat and the vehicle will slide, so it is necessary to record the real one and use the same one next time.

## Slide 60
NEW FEATURES
TRAJECTORY RECORDING
After recording the data, it is able to export data by SHP/ISOXML format.

## Slide 61
NEW FEATURES
IMPLEMENT SIGNAL INPUT
IMPLEMENT SIGNAL INPUT

## Slide 62
NEW FEATURES
IMPLEMENT SIGNAL INPUT
It is allowed to turn on input detection to enable/disable autopilot or track painting by implement different voltage signals.

## Slide 63
NEW FEATURES
TRACK PAINTING COLOR
TRACK PAINTING COLOR

## Slide 64
NEW FEATURES
TRACK PAINTING COLOR
Track painting color can support 6 colors right now.

## Slide 65
NEW FEATURES
3D VIEW & BRIGNTNESS
3D VIEW & BRIGNTNESS

## Slide 66
NEW FEATURES
3D VIEW & BRIGNTNESS
2D/3D view and Day/Night mode are supported.

## Slide 67
NEW FEATURES
MATERIALS
MATERIALS

## Slide 68
NEW FEATURES
MATERIALS
Manage spraying equipment and materials on this interface.

## Slide 69
NEW FEATURES
TROUBLESHOOTING
TROUBLESHOOTING

## Slide 70
NEW FEATURES
TROUBLESHOOTING
When encountering a malfunction, please check the information of each module on this interface and provide it to EFIX engineers.

## Slide 71
NEW FEATURES
BOOT GUIDE
BOOT GUIDE

## Slide 72
NEW FEATURES
BOOT GUIDE
It is necessary to enter the corresponding dealer code andlanguage to enter the software.

## Slide 73
NEW FEATURES
HANDLE
HANDLE/MULTI-FUNCTION BUTTON

## Slide 74
NEW FEATURES
HANDLE
1. Able to check status & version number
2. Able to customize the feature

## Slide 75
NEW FEATURES
PRIVACY SECURITY
PRIVACY SECURITY

## Slide 76
NEW FEATURES
PRIVACY SECURITY
Muliple items with password protection

## Slide 77
NEW FEATURES
ONE-CLICK UPDATE
ONE-CLICK UPDATE

## Slide 78
NEW FEATURES
ONE-CLICK UPDATE
After connecting to the Internet, the software will automatically detect updateable software or firmware, automatically download the latest version and update it.

## Slide 79
NEW FEATURES
PARAMETERS ADJUSTMENT
PARAMETERS ADJUSTMENT

## Slide 80
NEW FEATURES
PARAMETERS ADJUSTMENT
Adjust Online Aggressiveness, WAS GAIN and other parameters

## Slide 81
NEW FEATURES
NEW GUIDELINE MODES
NEW GUIDELINE MODES

## Slide 82
NEW FEATURES
NEW GUIDELINE MODES
1. Looped guideline
2. Whole area path line

## Slide 83
NEW FEATURES
NEW GUIDELINE MODES
1. Need 4 points
2. All are with Auto modes
NEW GUIDELINE MODES---WHOLE AREA PATH LINE

## Slide 84
NEW FEATURES
NEW GUIDELINE MODES
1. Need 4 points
2. All are with Auto modes
NEW GUIDELINE MODES---LOOPED LINE

## Slide 85
Yield more with less
Thank You